Cross section, ‘interaction cross section’ is the interaction strength between two particles. Represented by an area σ transverse on their relative movement. It ‘feels’ the electromagnetic field of atoms or electrons.

- The probabillity of an interaction where N particles move towards an area Σ with n atoms.

- Number of interacting particles

Differential cross section is about the probability to find a particle within Takes in account energy and direction. Either in rad or in sterad. “When you use this energy, there is a chance of finding the scattered photon within this angle”.

Photon interactions can occur by abortion or scattering. Coherent (elastic) or incoherent (inelastic).

Rayleigh scattering occurs without energy loss, coherent scattering. Photon is absorbed and re-emitted with a small angle. The atomic cross section is

Compton scattering is incoherent scattering. . The electron is assumed free from the atom, unbound. Given the atomic cross section

where er atom number and σ is the electron cross section. Differential cross section is

The higher the energy the higher the probability of forward scattering photon. And the electron scatter angle is related to the photon by

The Compton edge is the max energy transferred to the electron. And ends abruptley, though in real experiments it is smudged out because of doppler broadening. It is because the photon has a momentum distribution.
In addition the binding energy of the atom has to be included in the calculation, which is higher for high Z. It is more ‘prominent’ in high Z low hν.
In a Compton scatter the photon will always retain some energy.